HASviolet
Build Guide

Hudson Valley Digital Network
5 March 2020
v1.0
# Introduction
This build guide will walk you through the required hardware and software installation for HASviolet to function. HASviolet will require Internet connectivity via its onboard WiFi for update of the Raspbian Lite OS as well as use future use as a possible LoRaWAN gateway.

While the production of this guide and steps is focused on Linux users, references to
installation on Mac OSX and Windows platforms are called out within the text

All reference to “RPi” in this guide are an abbreviation for the Raspberry Pi Zero WH hardware.
# Hardware
HASviolet consists of the following hardware:

Raspberry Pi Zero WH (Wireless with Headers) / You will need to solder the 20-pin header to the board.
Adafruit LoRa Radio Bonnet with OLED – RFM95W @915Mhz / Antenna is via a male U.FL connector
SanDisk Ultra 16GB RAM Class 10 MicroSD / RPI require quality microSD cards at least Class 10
Power Source 5V @ 2.5A minimum / The hardware can be powered via USB to PC as part of setup but for operation it needs to be on a standalone power source
900 MHz Antenna with / U.FL IPEX to SMA Connector / We will use a simple omnidirectional antenna to get started. Permanent installations should use antennas with greater gain

# Preparing Media
Media installation and preparation for operating systems other than Linux can be found in the Raspberry Pi Documentation Section on Installing images.
From your PC insert an SD Card / Run sudo gparted partitioning software / From Gparted menu select Devices and SD card inserted / Unmount the SD card Delete any existing parititons / Right click on unallocated, select new, select FAT32 as file system. Click add / Click check mark to apply all operations
Download Raspbian and Extract from ZIP file / Install Raspbian on freshly formatted SD card	wget --max-redirect=3 https://downloads.raspberrypi.org/raspbian_lite_latest / unzip raspbian_lite_latest / sudo dd bs=4M if=2020-02-05-raspbian-buster-lite.img of=/dev/sdg conv=fsync

# Pi Connectivity
Via connected keyboard, monitor and mouse
Change to your home directory, run sync as sudo, and unmount the SD card / Remove the SD card	cd ~ / sudo sync / umount /media/sd-card/root / umount /media/sd-card/boot
You will rerquire a mini HDMI adapter to your monitor (HDMI, VGA, mDP, etc) / You will require a USB OTG cable to attach a keybaord

Via IP through Wireless Connection
You can use this method if you wish to access the RPi via an existing WiFi network / Change to the boot directory on the SD card / Enable ssh access by creating a blank file named ssh	cd /media/sd-card/boot / touch ssh
Within the boot directory, create a file called wpa_supplicant.conf and edit	vi wpa_supplicant.conf
When you have opened the new file, add the configuration at right and save / Be sure to replace SSID with your local wireless network SSID	country=US / ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev / update_config=1 / network={ / ssid="MyWiFiNetwork" / psk="aVeryStrongPassword" / key_mgmt=WPA-PSK / }
Change to your home directory, run sync as sudo, and unmount the SD card / Remove the SD card	cd ~ / sudo sync / umount /media/sd-card/root / umount /media/sd-card/boot

Via IP through USB connection
If WiFi is not available is is possible for the Pi to be IP accessible via USB from a desktop/laptop that runs zero-configuration networking, namely BonJour Services developed by Apple. method is for when access to a network is not possible for the Rpi but network access is possible from a laptop or PC.

For Linux add a USB Network Interface and a network with the Pi on the USB interface. Give it a static address (ie 169.254.15.1 )
Change to the boot directory on the SD card / Edit the config.txt file	cd /media/sd-card/boot / vi config,txt / Append the following line: / dtoverlay=dwc2 / Then save the file.
While in the boot directory, edit the cmdline.txt file, replace a line, then save file.	vi cmdline,txt / Replace with the following all as one continuous line: / dwc_otg.lpm_enable=0 console=serial0,115200 console=tty1 root=/dev/mmcblk0p2 rootfstype=ext4 elevator=deadline fsck.repair=yes rootwait modules-load=dwc2,g_ether quiet init=/usr/lib/raspi-config/init_resize.sh / Than save the file.
Remaining in the boot directory, enable ssh access by creating a blank file named ssh	touch ssh
Change to the rootfs directory / Edit the interfaces file	cd /media/sd-card/rootfs/etc/network / vi interfaces / Append the following lines: / allow-hotplug usb0 / iface usb0 inet static / address 169.254.15.2 / netmask 255.255.255.0 / network 169.254.15.0 / broadcast 169.254.15.255 / gateway 169.254.15.1 / Then save the file
Change to your home directory, run sync as sudo, and unmount the SD card / Remove the SD card	cd ~ / sudo sync / umount /media/sd-card/root / umount /media/sd-card/b

# Pi Setup
Install Adafruit Radio Bonnet and Antenna / Insert SD card / Connect RPI and Power on / Log in with default pi:raspberry	If accessing via IP over USB, connect PC USB port to RPi USB Data port (next to mini-HDMI port) / ssh -l pi <yourpi> / If connecting via SSH for first time click yes to accept fingerprint
Run Configuration tool	sudo raspi-config
Navigate through each menu making selections as noted then exit tool	1. Change User Password to <something> / 2. Network options / N1 Change hostname to your call + number [1-15] / yourcall-5 / 3. Boot Options / B1 Desktop/CLI / choose B1 Console / 4. Localization / I1 Change Local to en_US.UTF-8 / I2 Change Timezone / I4 Set to US / 5. Interfacing options / P2 Enable SSH / P4 Enable SPI / P5 Enable I2C / 7. Advanced Options / A3 memory Split / Reduce GPU from 64 to 16 / 8. Update
Run sync as sudo, and reboot	sudo sync ; sudo sync ; sudo sync / sudo reboot

# HASviolet Install
Copy Report and Run Install
Ensure you are in the home directory / Install Git / Clone the Github HASviolet repo locally / Go into the build directory and run the install shell script	cd ~ / sudo apt-get install -y git / mkdir hvdn-repo ; cd hvdn-repo / git clone https://github.com/hudsonvalleydigitalnetwork/hasviolet.git / cd hasviolet/build / ./hvdn_hasviolet_install.sh
Installation is complete. Apps are run from /home/pi/hvdn	Installed Directories include / /home/pi/hvdn where the programs and their config files are to be run from / /home/pi/hvdn-repo is local repo of hvdn apps are / /home/pi/hvdn-repo/hasviolet is local repo of HASviolet

# Using HASviolet
HVDN Communicator is data only currently designed to be used on local LoRa networks. It is installed in /home/pi/hvdn-comm

HVDN Communicator is built with Python. Applications include;

- hvdn_lora-beacon.py sends a repeating broadcast message
- hvdn_lora-chat.py is a half-duplex messaging app
- hvdn_lora-tx.py sends a message to another LoRa station
- hvdn_lora-rx.py listens for messages from other LoRa stations

Three files dependend by all applications are;

- hvdn-comm.ini is a configuration file
- rf95.py is a Python Library for the HOPE RFM95 modules on the Raspberry Radio Bonnet
- font5x8.bin used by the OLED on the Adafruit Radio Bonnet

### hvdn_lora-beacon.py
Beacon a LoRa message
Usage: hvdn_lora-beacon.py -c COUNT -t DELAY "message"

OPTIONS
        -c Number of times to repeat MESSAGE
        -t NUmber of seconds before repeat MESSAGE
        MESSAGE is message to be send within double quotes
### hvdn_lora-chat.py
Half-duplex LoRa messaging app
Usage: ./hvdn_lora-chat [-r] [-s]

OPTIONS
    -h, --help show this help message and exit
    -r, --raw_data Receive raw data
    -s, --signal Signal Strength
- Starts and loops in Listening Mode
- CTRL-Z to send a message, CTRL-C to exit program
- When in send mode
  - Recipient is node id (255 = broadcast address)
  - Message is whatever message followed by enter
  - Message is sent, return to listening mode
### hvdn_lora-tx.py
Send a LoRa message
Usage: hvdn_lora-tx.py -d DESTINATION "message"

OPTIONS
        -d Destination ID
        MESSAGE is message to be send within double quotes
### hvdn_lora-rx.py
Listens for messages from other LoRa stations
Usage: ./hvdn_lora-rx.py -r -s

OPTIONS
    -h, --help show this help message and exit
    -r, --raw_data Receive raw data
    -s, --signal Signal Strength

# HASviolet Manual Install
The build script (hvdn_hasviolet_install.sh) automates the following steps.

Install Raspbian Packages
Log back into the RPi. / Ensure you are in the home directory / Install the following packages / pip3 – Python Package Index / Git – For cloning repositories	cd ~ / sudo apt-get install python3-pip / sudo apt-get install git

Install Python Libraries
Install the following Python libraries / Python Image Library / APRS and APRSlib / Adafruit Radio Bonnet Libraries	sudo apt-get install python3-pil / sudo pip3 install aprs / sudo pip3 install aprslib / sudo pip3 install adafruit-circuitpython-rfm69 / sudo pip3 install adafruit-circuitpython-rfm9x / sudo pip3 install adafruit-circuitpython-ssd1306 / sudo pip3 install adafruit-circuitpython-framebuf
Install HVDN Repository
Ensure you are in the home directory / Make two new directories called hvdn and hvdn-repo / Change directory to hvdn-repo and clone the HASViolet repo from Github / Copy the HASviolet stable directory to hvdn	cd ~ / mkdir hvdn-comm / mkdir hvdn-repo / cd hvdn-repo / git clone https://github.com/hudsonvalleydigitalnetwork/hasviolet.git / cp -R /home/pi/hvdn-repo/hasviolet/stable/* /home/pi/hvdn
Installation is complete. Apps are run from /home/pi/hvdn	Installed Directories include / /home/pi/hvdn where the programs and their config files are to be run from / /home/pi/hvdn-repo is local repo of hvdn apps are / /home/pi/hvdn-repo/hasviolet is local repo of HASviolet