HVDN Communicator
Linux Distro Build Guide

Hudson Valley Digital Network
7 February 2020
v0.7
# Introduction
This is a guide on how to build the distribution image for the HVDN Communicator. All reference to “RPi” in this guide are an abbreviation for the Raspberry Pi Zero W hardware. The desktop operating system used in preparing the build is assumed to be a Debian or Debian derivative distribution. Ubuntu 18.04 was use din the preparation of this guide.

# Preparing Media
From your PC mount an 8GB SD Card / Run sudo gparted partitioning software / From Gparted menu select Devices and SD card inserted / Any existing partitions on the SD card right click and select Delete / Right click on unallocated, select new, select FAT32 as file system. Click add / Click check mark to apply all operations / Note only up to 8GB of the SD Card will be formatted
Download Raspbian and Extract from ZIP file / Install Raspbian on freshly formatted SD card	wget --max-redirect=3 https://downloads.raspberrypi.org/raspbian_lite_latest / unzip raspbian_lite_latest / sudo dd bs=4M if=2019-09-26-raspbian-buster-lite.img of=/dev/sdg conv=fsync

# Pi Connectivity
Via connected keyboard, monitor and mouse
Change to your home directory, run sync as sudo, and unmount the SD card / Remove the SD card	cd ~ / sudo sync / umount /media/sd-card/root / umount /media/sd-card/boot

Via IP through Wireless Connection
You can use this method if you wish to access the RPi via an existing WiFi network / Change to the boot directory on the SD card / Enable ssh access by creating a blank file named ssh	cd /media/sd-card/boot / touch ssh
Within the boot directory, create a file called wpa_supplicant.conf and edit	vi wpa_supplicant.conf
When you have opened the new file, add the configuration at right and save / Be sure to replace SSID with your local wireless network SSID	country=US / ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev / update_config=1 / network={ / ssid="MyWiFiNetwork" / psk="aVeryStrongPassword" / key_mgmt=WPA-PSK / }
Change to your home directory, run sync as sudo, and unmount the SD card / Remove the SD card	cd ~ / sudo sync / umount /media/sd-card/root / umount /media/sd-card/boot

Via IP through USB connection
In this configuration you will be powering the RPi via the USB cable to your PC. Be sure to use the correct USB cable / On your Linux host you need to add a USB Network Interface and a network with the Pi on the USB interface. Give it a static address (ie 169.254.15.1 )
Change to the boot directory on the SD card / Edit the config.txt file	cd /media/sd-card/boot / vi config,txt / Append the following line: / dtoverlay=dwc2 / Then save the file.
While in the boot directory, edit the cmdline.txt file, replace a line, then save file.	vi cmdline,txt / Replace with the following all as one continuous line: / dwc_otg.lpm_enable=0 console=serial0,115200 console=tty1 root=/dev/mmcblk0p2 rootfstype=ext4 elevator=deadline fsck.repair=yes rootwait modules-load=dwc2,g_ether quiet init=/usr/lib/raspi-config/init_resize.sh / Than save the file.
Remaining in the boot directory, enable ssh access by creating a blank file named ssh	touch ssh
Change to the rootfs directory / Edit the interfaces file	cd /media/sd-card/rootfs/etc/network / vi interfaces / Append the following lines: / allow-hotplug usb0 / iface usb0 inet static / address 169.254.15.2 / netmask 255.255.255.0 / network 169.254.15.0 / broadcast 169.254.15.255 / gateway 169.254.15.1 / Then save the file
Change to your home directory, run sync as sudo, and unmount the SD card / Remove the SD card	cd ~ / sudo sync / umount /media/sd-card/root / umount /media/sd-card/b

# Initial Pi Setup
Install Adafruit Radio Bonnet and Antenna / Insert SD card / Connect RPI and Power on / Log in with default pi:raspberry	If accessing via IP over USB, connect PC USB port to RPi USB Data port (next to mini-HDMI port) / If connecting via SSH for first time click yes to accept fingerprint
Run Configuration tool	sudo raspi-config
Navigate through each menu making selections as noted then exit tool	1. Change User Password to <something> / 2. Network options / N1 Change hostname to your call + number [1-15] / yourcall-5 / 3. Boot Options / B1 Desktop/CLI / choose B1 Console / 4. Localization / I1 Change Local to en_US.UTF-8 / I2 Change Timezone / 5. Interfacing options / P2 Enable SSH / P4 Enable SPI / P5 Enable I2C / 7. Advanced Options / A3 memory Split / Reduce GPU from 64 to 16 / 8. Update
Run sync as sudo, and reboot	sudo sync / sudo reboot

# HAS Violet Install
A build script has been provided on the GitHub HAS Violet repo in the build directory (hvdn_hasviolet_install.sh) that automates the following sections. You have the option of running it or following the instructions in the following sections.

Install Raspbian Packages
Log back into the RPi. / Ensure you are in the home directory / Install the following packages / pip3 – Python Package Index / Git – For cloning repositories	cd ~ / sudo apt-get install python3-pip / sudo apt-get install git

Install Python Libraries
Install the following Python libraries / Python Image Library / APRS and APRSlib / Adafruit Radio Bonnet Libraries	sudo apt-get install python3-pil / sudo pip3 install aprs / sudo pip3 install aprslib / sudo pip3 install adafruit-circuitpython-rfm69 / sudo pip3 install adafruit-circuitpython-rfm9x / sudo pip3 install adafruit-circuitpython-ssd1306 / sudo pip3 install adafruit-circuitpython-framebuf
Install HVDN Repository
Ensure you are in the home directory / Make two new directories called hvdn-comm and hvdn-repo / Change directory to hvdn-repo and clone the HASViolet repo from Github / Copy the HASviolet stable directory to hvdn-comm	cd ~ / mkdir hvdn-comm / mkdir hvdn-repo / cd hvdn-repo / git clone https://github.com/hudsonvalleydigitalnetwork/hasviolet.git / cp /home/pi/hvdn-repo/hasviolet/stable /home/pi/hvdn-comm

# Using HVDN Communicator
HVDN Communicator is data only currently designed to be used on local LoRa networks. It is installed in /home/pi/hvdn-comm

HVDN Communicator is built with Python. Applications include;

- hvdn_lora-beacon.py sends a repeating broadcast message
- hvdn_lora-chat.py is a half-duplex messaging app
- hvdn_lora-tx.py sends a message to another LoRa station
- hvdn_lora-rx.py listens for messages from other LoRa stations

Three files dependend by all applications are;

- hvdn-comm.ini is a configuration file
- rf95.py is a Python Library for the HOPE RFM95 modules on the Raspberry Radio Bonnet
- font5x8.bin used by the OLED on the Adafruit Radio Bonnet

### hvdn_lora-beacon.py
Beacon a LoRa message
Usage: hvdn_lora-beacon.py -c COUNT -t DELAY "message"

OPTIONS
        -c Number of times to repeat MESSAGE
        -t NUmber of seconds before repeat MESSAGE
        MESSAGE is message to be send within double quotes
### hvdn_lora-chat.py
Half-duplex LoRa messaging app
Usage: ./hvdn_lora-chat [-r] [-s]

OPTIONS
    -h, --help show this help message and exit
    -r, --raw_data Receive raw data
    -s, --signal Signal Strength
- Starts and loops in Listening Mode
- CTRL-Z to send a message, CTRL-C to exit program
- When in send mode
  - Recipient is node id (255 = broadcast address)
  - Message is whatever message followed by enter
  - Message is sent, return to listening mode
### hvdn_lora-tx.py
Send a LoRa message
Usage: hvdn_lora-tx.py -d DESTINATION "message"

OPTIONS
        -d Destination ID
        MESSAGE is message to be send within double quotes
### hvdn_lora-rx.py
Listens for messages from other LoRa stations
Usage: ./hvdn_lora-rx.py -r -s

OPTIONS
    -h, --help show this help message and exit
    -r, --raw_data Receive raw data
    -s, --signal Signal Strength